## Slide 1: Product gas properties, gas cleaning and applications
Technische Universität Wien
Institute of Chemical, Environmental and Bioscience Engineering
Research Unit of Fuel and Energy System Engineering
Research Group for Industrial Plant Engineering and Application of Digital Methods
DI Dr. Florian Benedikt
florian.benedikt@tuwien.ac.at

## Slide 2: Vision of gasification technologies
2
residuals from agriculture
wood chips
residuals from
industry
residuals from municipalities
sewage sludge/
manure
heat
electricity
synthetic natural gas (SNG)
advanced biofuels
hydrogen
into clean energy carriers
CO2 as feedstock
conversion of biogenic raw and residual materials
platform chemicals
resources
products

## Slide 3: Dual fluidized bed (DFB) steam gasification: Product gas cleaning and selected applications
3

## Slide 4: Product gas properties: main gas composition
Main gas composition
H2
CO
CO2
CH4
N2
H2O
Resulting in:
H2/CO – ratio:
important for synthesis applications
Heating value (CH4 ~ 36 MJ/Nm³, CO ~ 12.6 MJ/Nm³, H2 ~ 10.8 MJ/Nm³)
mainly depending on
gasification agent (H2O, air, CO2, …)
reactor type
operation parameters (temperature, pressure, bed material…)
feedstock
 | Unit | Air gasification | Steam gasification
Calorific value | MJ/m3 | 4 - 6 | 12 - 14
H2 | vol.% | 11- 16 | 35 - 40
CO | vol.% | 13 - 18 | 25 - 30
CO2 | vol.% | 12 - 16 | 20 - 25
CH4 | vol.% | 3 - 6 | 9 -11
N2 | vol.% | 45 - 60 | <1

## Slide 5: DFB steam gasification main product gas composition from biogenic feedstock
Schmid, J.C., Benedikt, F., Fuchs, J., Mauerhofer, A.M., Müller, S., Hofbauer H., 2019, "Syngas for biorefineries from thermochemical gasification of lignocellulosic fuels and residues - 5 years’ experience with an advanced dual fluidized bed gasifier design". Biomass Conversion and Biorefinery,

## Slide 6: Product gas properties: impurities
Impurities
Particulate matter (fly dust/ash, fly char)
Tar “hydrocarbons with molecular weight higher than benzene”
Sulfur compounds (H2S, COS, …)
Nitrogen compounds (NH3, HCN, …)
Alkali compounds
Halides (HCl, …)
Resulting in:
Erosion, corrosion or deposits in downstream plant components
Gas cleaning due to compliance with emission limits or limits for downstream equipment (catalyst poisoning) or limits for end-users (grid feed-in, fuel cells, engines, …)
Schmid, J.C., Benedikt, F., Fuchs, J., Mauerhofer, A.M., Müller, S., Hofbauer H., 2019, "Syngas for biorefineries from thermochemical gasification of lignocellulosic fuels and residues - 5 years’ experience with an advanced dual fluidized bed gasifier design". Biomass Conversion and Biorefinery,

## Slide 7: DFB steam gasification product gas impurities (tar) from biogenic feedstock
Schmid, J.C., Benedikt, F., Fuchs, J., Mauerhofer, A.M., Müller, S., Hofbauer H., 2019, "Syngas for biorefineries from thermochemical gasification of lignocellulosic fuels and residues - 5 years’ experience with an advanced dual fluidized bed gasifier design". Biomass Conversion and Biorefinery,

## Slide 8: DFB steam gasification product gas impurities from biogenic feedstock
Schmid, J.C., Benedikt, F., Fuchs, J., Mauerhofer, A.M., Müller, S., Hofbauer H., 2019, "Syngas for biorefineries from thermochemical gasification of lignocellulosic fuels and residues - 5 years’ experience with an advanced dual fluidized bed gasifier design". Biomass Conversion and Biorefinery,
Parameter | Unit | SW | HNS | BA | SCB | RH | BA + CMa | CM | BA | BA + CM + STb | LI
Fly char | g/Nm3db | 1–3 | 1–2 | 7–10* | 4–9 | 5–7* | 1.5–3 | 0.5–1 | 2–4 | 1–1.5 | 0.5–2
Dust | g/Nm3db | 1–4 | 1–3 | 15–22* | 6–8 | 55–70* | 3–4 | 4–7 | 1–3 | 0.5–2 | 0.5–1
NH3 | vol ppm | n.m. | n.m. | 3300** | n.m. | 7600 | 23,800 | 73,200 | n.m. | 23,900 | n.m.
H2S | vol ppm | 17–23 | n.m. | 190–275 | n.m. | 460 | 360–480 | 340–390 | n.m. | 140 | n.m.
COS | vol ppm | 0.1–0.7 | n.m. | 0.3–0.7 | n.m. | n.m. | 13–16 | 25–61 | n.m. | n.m. | n.m.
HCl | vol ppm | n.m. | n.m. | 0.6** | n.m. | n.m. | n.m. | n.m. | n.m. | 14 | n.m.
HCN | vol ppm | n.m. | n.m. | n.m. | n.m. | n.m. | n.m. | n.m. | n.m. | 400 | n.m.
SW, softwood; HNS, hazelnut shells; BA, bark;
SCB, sugarcane bagasse; RH, rice husk;
CM, chicken manure; ST, straw; LI, lignin;
n.m., not measured
*High content because the cyclone downcomer clogged
**Value from a similar test run with bark
a70% BA and 30% CM based on weight
b60% BA and 25% CM and 15% ST based on weight

## Slide 9: Product gas cleaning: classification according to temperature
T ≤ ambient temperature
100°C < T < 400°C
T > 400°C
Woolcock, P. J., & Brown, R. C. (2013) “A review of cleaning technologies for biomass-derived syngas. Biomass and Bioenergy” , 52, 54–84.
Malicha, M., 2018, "Design of gas cleaning processes for SNGproduction from biogenic residues", Diplomarbeit, TU Wien, Oktober 2018

## Slide 10: Operation conditions of hydrogen production, SNG and FT-synthesis
Molino A, Larocca V, Chianese S, Musmarra D. “Biofuels Production by Biomass Gasification: A Review”, Energies 2018;11(4):811.
Product | Pressure | Temperature | Catalyst | H2/CO | H2/CO2
Unit | bar | °C | - | mol/mol | mol/mol
Hydrogen | 1-30 | 200-1100 | Ni, Fe, Mo catalysts | -a | -
SNG | 1-25 | 200-450 | Ni (mainly), Co, Fe, Ru catalysts | ≥ 3 | 4
FT products | 10-40 7-12 | 300-350 200-240 | Fe catalyst Co catalyst | 0.6–1.7; 2b 2.0–2.15 | 1; 3b 3
a H2O/CO ≥ 2 │ b Using potassium as promoter
CO-methanation
CO2-methanation

## Slide 11: Limits of product gas impurities for selected applications
Contaminant | Unit | Syngas applications |  |  |  |  | Gas turbine | Gas engine
 |  | MeOH | EtOH | FT | H2 | SNG |  | 
Particulate matter | mg/Nm3 | <0.02 | 0 | 0 | 0 | 0 | <20-30 | <50
Tar | mg/Nm3 | <0.01 | <0.5a | <0.1 -1 | <1-2 | <5 | <5-10 | <100
Alkali compounds | ppmv | <0.005 | n.a. | <0.01 | n.a. | n.a. | <0.02 -0.05 | <0.1b
N-contaminants | ppmv | <0.1-10 | <1-10 | <0.02 -10 | <1-10 | <30 | <50 | n.a.
S-contaminants | ppmv | <0.5 | <1-50 | <0.01 | <1-50 | <0.1c | <1-20 | <20
Halides | ppmv | <0.001 | n.a. | <0.01 | n.a. | <10 | <0.5-1 | n.a.
Veress M. “Optimization of a process concept for the industrial production of Bio-SNG from low-grade fuels”, master thesis, Vienna, TU Wien, 2020.
n.a. = not available │ a in ppmv │ b in mg/Nm³ | c for Ni-catalysts
Molino A, Larocca V, Chianese S, Musmarra D. “Biofuels Production by Biomass Gasification: A Review”, Energies 2018;11(4):811.

## Slide 12: Product gas cleaning DFB steam gasification for gas engine application
removes particles, alkalines, tar
removes tar, water, HCl, NH3
800-850°C
~150°C
~40°C

## Slide 13: Project „ReGas4Industry“
13
Efficient and cost-effective conversion of biogenic residues to synthetic natural gas (SNG) via gasification and catalytic methanation.
Targets:
Utilization of biogenic residues for SNG production
Novel reactor/process concepts for a simplified and efficient conversion
Fundamental knowledge to support scale-up
Cost reduction
Duration: 04/2019 – 09/2021
Status: Ongoing

## Slide 14: „ReGas4Industry“ experimental approach at TU Wien
14
alternative fuels
gas cleaning
DFB steam/CO2 gasification
methanation
SNG from biogenic residues
Technoeconimic and ecological assessment
sewage sludge
reject
bark
digestate
SNG

## Slide 15: „ReGas4Industry“ basic flow sheet
15
100 kW DFB Gasification
10 kW SNG process chain
Biodiesel scrubber
Activated carbon filter
ZnO guard filter
Fluidized bed methanation

## Slide 16: DFB Gasifier, biodiesel scrubber and adsorption unit
16

## Slide 17: Fluidized bed methanation
17

## Slide 18: Vision of gasification technologies
18
residuals from agriculture
wood chips
residuals from
industry
residuals from municipalities
sewage sludge/
manure
heat
electricity
synthetic natural gas (SNG)
advanced biofuels
hydrogen
into clean energy carriers
CO2 as feedstock
conversion of biogenic raw and residual materials
platform chemicals
resources
products

## Slide 19: Product gas properties, gas cleaning and applications
Technische Universität Wien
Institute of Chemical, Environmental and Bioscience Engineering
Research Unit of Fuel and Energy System Engineering
Research Group for Industrial Plant Engineering and Application of Digital Methods
DI Dr. Florian Benedikt
florian.benedikt@tuwien.ac.at